## Slide 1: Operating Systems
1
7. Memory Management

## Slide 2: Memory Management
Ideally programmers want memory that is
  Large
  Fast
  Non volatile
Memory hierarchy
  Small amount of fast, expensive memory – cache
  Some medium-speed, medium price main memory
  Gigabytes of slow, cheap disk storage
Memory manager handles the memory hierarchy

## Slide 3: Requirements for Memory Management Unit (MMU)
Relocation
  Change the physical placement of a process
Protection
  Restrict processes access to physical memory
Sharing
  Allow processes to share memory location
Logical Organization
  Support organization of computer programs etc.
Physical Organization
  Efficient utilization of hardware
  Memory hierarchy

## Slide 4: Background
Program
Typically resides on disk
Must be brought into memory to be executed
Address binding of a program
Compile time
  Program must always be loaded to the same memory location
Load time
  Memory location determined when program is loaded
Run time/ Execution time
  No absolute memory locations
  Memory location determined by memory management unit (MMU)
    Swapping of processes and relocation

## Slide 5: Background
Memory
Can be subdivided to accommodate multiple processes
Needs to be allocated efficiently to pack as many processes into memory as possible

## Slide 6: Position and Function of the MMU
Logical address: Generated by the CPU
  Also referred to as virtual address or relative address
Physical address: Address seen by the memory unit
  Also referred to as absolute address

## Slide 7: Sharing Memory Through Swapping
A process can be swapped out of memory to a backing store
– Swap device
Later brought back (swap-in) into memory for continued execution

## Slide 8: Relocation and Protection
Relocation
Swapping
  Program must be relocated
Cannot be sure about the location in memory
Addressing
  No absolute addressing feasible
  For example, locations of variables, code routines
Protection
Must keep a program out of other processes’ partitions

## Slide 9: Hardware Support For Relocation and Protection
Base, bounds (limit) registers
  Define the range which a process can access
  Set when the process is executing

## Slide 10: Hardware Support For Relocation and Protection
System
Partition 1 Operating
Partition 3
800K
Partition 4
700K
400K
Partition 2
200K
100K
0
Base Register
Limit Register
Adder
Comparator
Relative Address
Absolute Address
Interrupt
Addition and comparison has to be performed on every address
Memory Management Unit (MMU)
Logical Address
Physical Address

## Slide 11: Contiguous Allocation of Memory: Fixed Partitioning
Any program, no matter how small, occupies an entire partition
Causes internal fragmentation
  Allocated memory can be larger than requested memory
  Difference internal to a partition, but not being used by the process

## Slide 12: Fixed Partitioning
Multiple Queues
Small processes have to wait, even though plenty of memory is free
  When a large partition is empty
  Queues for small partition is full
Alternative: Maintain a single Queue

## Slide 13: Fixed Partitioning
Single Queue
Whenever a partition becomes free, a process is selected
  Closest to the front of the queue
  Smaller than the partition size
Undesirable to waste a large partition for smaller process
  Search the queue, find the largest process that fits it
Unfair for smaller processes
  A process may not be skipped more than k times
System
Partition 1 Operating
Partition 2
Partition 3
Partition 4
800K
700K
400K
200K
100K
0

## Slide 14: Contiguous Allocation: Dynamic Partitioning
Process is allocated exactly as much memory as required
Eventually holes in memory: External fragmentation
  Total memory space exists to satisfy a request
  But it is not contiguous
Must use compaction to shift processes (defragmentation)

## Slide 15: Memory Management With Bitmaps
Memory is divided up into allocation units
  Few words
  Or several kilobytes
. . .
8
16
24
C
B
D
E
A.
... … …
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0

## Slide 16: Memory Management With Bitmaps
Size of allocation unit is important
Smaller allocation unit
  Larger bitmap required
Larger allocation unit
  Smaller bitmap required
  More memory will be wasted
    If the process size is not an exact multiple of the allocation unit

## Slide 17: Memory Management With Bitmaps
To bring a k unit process in memory
Search for a k run consecutive 0 bits in the map
Search can be slow
Since, k run may cross word boundaries
... … …
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
Find run of length = 3
Find run of length = 4

## Slide 18: Memory Management with Linked Lists
Linked list of memory segments
  Free segments  Holes
  Allocated segments  Processes
. . .
8
24
E
A.
P 0
5 .
B C D 16
H 5 3 P 8 6
P 14
H 18 2
P 20 6
4 .
P 26 3

## Slide 19: Memory Management with Linked Lists
Segment list is sorted by addresses
Sorting helps in updating the list, when a process is swapped out or exits
A process usually has two neighbors
Updating the list requires
. . .
A
B
X
. . .
A
B

Replace P by H
. . .
A
X
. . .
A


Two entries are merged
. . .
B
X
. . .
B
Two entries are merged
. . .
X
. . .

Three entries are merged

## Slide 20: Dynamic Partitioning: Placement Algorithms
First-fit: Use the first block that is big enough
– Simple and fast

## Slide 21: Dynamic Partitioning: Placement Algorithms
Next-fit: Use the next block that is big enough
  Tends to eat-up the large block at the end of the memory
  Gives no better performance than First-fit

## Slide 22: Dynamic Partitioning: Placement Algorithms
Best-fit: Use the smallest block that is big enough
  Must search entire list (unless free blocks are ordered by size)
  Produces the smallest leftover hole
    Tends to fill up memory, with tiny useless holes
    First Fit generates larger holes on the average

## Slide 23: Dynamic Partitioning: Placement Algorithms
Worst-fit: Use the largest block
  Must also search entire list
  Produces the largest leftover hole…
  … but eats-up big blocks

## Slide 24: Memory Management with Linked Lists
Search time of all four placement algorithms can be improved by
  Keeping separate lists for Process and Holes
  While allocating memory only have to search the lists of holes
  The Hole list can be kept sorted by size
    As soon as a hole that fits is found, no more searching is required
Drawback
  Problem while de-allocating memory
  A node from the process list has to be inserted in the hole list

## Slide 25: To Avoid External Fragmentation: Paging
Partition memory into small equal-size chunks (frames)
Divide each process into the same size chunks (pages)
OS maintains a page table for each process
  Contains the frame location for each page in the process
  Memory address = (page number, offset within page)

## Slide 26: Page Example: Allocation of Frames

## Slide 27: Paging Example
Pages of a process form the logical memory
Maintain for each process a page table
Question: Do we avoid fragmentation completely?

## Slide 28: Typical Page Table Entry
Present/Valid: value valid to be used, otherwise page fault
Protection: defines accesses which are permitted
Referenced: help to decide which frames can be reclaimed
Caching: Needed if value is read from I/O device
Modified: Needed if page frames are reclaimed
– Dirty: Needs to be written to disk first
Exact layout is hardware dependent

## Slide 29: Paging Example
7-Memory
29
16k-20k
12k-16k
8k –12k 4k – 8k 0k – 4k
5 1
1
0
1
1
1
0
1
0
0
0
20k-24k
16k-20k
12k-16k
8k –12k 4k – 8k 0k – 4k
1
0
1
0
12k-16k
8k –12k 4k – 8k 0k – 4k
P1 3 X 1
6
P2 0 X 2 X X X
P3
4
X 7 X
0
1
2
3
4
5
6
7
Physical Address Space (RAM)
0k – 4k 4k – 8k 8k –12k 12k-16k
14k-20k
20k-24k
24k-28k
28k-32k
Present bit

## Slide 30: Address Translation Scheme
Address generated by CPU is divided into two parts
Page number (p) – used as an index into a page table which contains base address of each page in physical memory
Page offset (d) – combined with base address to define the physical memory address that is sent to the memory unit
For given logical address space 2m and page size 2n
page number
p m - n
page offset
d n

## Slide 31: Address Translation Scheme
Size of logical address space = 2m
  # of pages (2m-n)× page size (2n)
Example: 16 X 4096
  2m = 24 X 212
  2m = 216
  m = 16 bits
page number
p m - n
page offset
d n

## Slide 32: Address Translation Scheme: Example
Given m=16 and n=12
Page number = m-n bits = Leftmost 4 bits
– 4 bit page number can represent 16 pages
Page offset = n bits = Rightmost 12 bits
  12 bit offset can address all 4096 bytes within a page (Frame size) !!
Consider logical address 8196 = 0010000000000100
– Page number is 2 and offset is 4
page number
p m - n
page offset
d n

## Slide 33: Address Translation Scheme: Example

## Slide 34: Address Translation Scheme: Example
Consider an address of m = 16 and n = 10 bits
  Leftmost m-n bits are page number
  Rightmost n bits are the offset
Given a logical address 0000010111011110
  Page number is 1 and offset 478
Suppose this page is residing in main memory frame 6 (000110)
  Physical address is frame number 6, offset 478
page number
p m - n
page offset
d n

## Slide 35: Implementation of Page Table – Main Memory
Page table is kept in main memory
  Page-table base register (PTBR) points to the page table
  Page-table length register (PRLR) indicates size of the page table
Each program reference to memory  2 memory accesses

## Slide 36: Implementation of Page Table – Associative Memory
Translation Lookaside Buffers (TLBs)
  Special fast-lookup hardware cache
  Parallel search (cache for page table)
  Resides usually inside the MMU
Address translation (P, O)
  If P is in associative register (hit)
  Get frame # from TLB
  Else get frame # from page table in m

## Slide 37: Paging Hardware With TLB

## Slide 38: Access Time With Cache Registers
Associative Lookup = s time units (fraction of microsecond)
  Can be < 10% of memory access time
Hit ratio (= α)
  Percentage of times a page number is found in associative registers
Effective Access Time = (1 + s) α + (2 + s)(1 – α) = 2 + s – α
  Assume memory cycle time is 1 microsecond
Example:
  Consider α = 80%, s = 20ns for TLB search, 100ns for memory access
  Effective access time = 0.80 * 120 + 0.20 * 220 = 140 ns

## Slide 39: Single-Level Page Table Limitation
Consider a system with
  32-bit logical address space
  4KB frame size
How many entries will be in the (single-level) page table?
  220 (1 million) entries
Each entry of page table consists of 4 bytes
  What will be the size of (single-level) page table?
    4MB
page number
p m - n
page offset
d n

## Slide 40: Two-Level Page-Table Scheme
Page-table may be large, i.e., occupy several pages/frames itself

## Slide 41: Address Translation in Two-Level Memory
Assume byte level addressing
– 232 bytes = 222kbytes = 212Mbytes = 4Gbytes can be supported
210 page frames can be addressed

## Slide 42: Multi-Level Page Table
p1
42
p2
10
d
12
Even two-level paging scheme might not be sufficient
Consider a system with 64-bit logical address space
  Frame size is 4 KB (212)
How many entries in single-level page table?
  Page table has 252 entries
How many entries in two-level page table
outer page inner page page offset

## Slide 43: Multi-Level Page Table
How many entries in three level page table?
How many levels are require such that each page table fits within a single frame?

## Slide 44: Inverted Page Table
One entry for each page frame of real memory
Entry consists of
  Virtual address of the page stored in that real memory location,
  With information about the process that owns that page
Decreases memory needed to store each page table
But increase in time needed to search the table when a page reference occurs
Use hash table to limit the search to one — or at most a few — page-table entries

## Slide 45: Inverted Page Table Example

## Slide 46: Chapter Overview
Background
Memory allocation schemes
  Fixed partition
  Dynamic partition
  Paging
Virtual memory

## Slide 47: Execution of a Program: Virtual Memory Concept
Main memory = cache of the disk space
Operating system brings into main memory a few pieces of the program
Resident set - portion of process that is in main memory
Whenever an address is needed that is not in main memory
  Generation of a page-fault interrupt
  OS places the process in blocking state and issues a disk IO request
  Another process is dispatched

## Slide 48: Valid-Invalid (Present/Absent) Bit
With each page table entry a valid–invalid bit is associated
– 1  in-memory
– 0  not-in-memory (Initially 0)
Frame #
valid-invalid bit
1
1
1
1
0

0
0
Page table
During address translation, if valid-invalid bit in page table entry is 0
– Page fault interrupt to OS

## Slide 49: Page Fault and Address Translation
7-Memory 49
In response to page-fault, paging hardware issue trap to OS
Check validity of memory reference
Get empty frame (swap out that page?)
Swap in page into frame
Reset tables, validation bit
Restart instruction

## Slide 50: If There is No Free Frame?
Page replacement
Goal: Algorithm which will result in minimum number of page faults
Page fault forces choice
  Which page must be removed
  Make room for incoming page
Modified page must first be saved
  Unmodified just overwritten (use dirty bit to optimize writes to disk)
Better not to choose an often used page
  Will probably need to be brought back in soon

## Slide 51: First-In-First-Out (FIFO) Replacement Algorithm
Can be implemented using a circular buffer
Example: Reference string: 1, 2, 3, 4, 1, 2, 5, 1, 2, 3, 4, 5
– 3 frames
– 4 frames
Belady’s Anomaly: More frames, sometimes more page faults
– Problem: replaces pages that will be needed soon
1 4 5
1 3 9 page faults
2 4
1
2
3
4
5 4
1 5 10 page faults
2
3

## Slide 52: Optimal Replacement Algorithm
Replace page that will not be used for longest period of time
4 frames example
– 1, 2, 3, 4, 1, 2, 5, 1, 2, 3, 4, 5
How can we know this information?
Standard for measuring how well other algorithms perform
1 | 4 | 
2 |  | 6 page faults
3 |  | 
4 | 5 | 

## Slide 53: Least Recently Used (LRU) Replacement Algorithm
Idea: Replace the page that has not been referenced for the longest time
  By the principle of locality, this should be the page least likely to be referenced in the near future
Implementation
  Tag each page with the time of last reference
  Use a stack
Problem
  High overhead
  OS kernel involvement at every memory reference!!!
    If hardware support not available

## Slide 54: LRU Algorithm
4 frame example
– 1, 2, 3, 4, 1, 2, 5, 1, 2, 3, 4, 5
1
2
3
4
5
5 4
3
8 page faults

## Slide 55: LRU Approximations: Clock/Second Chance
Uses reference (use) bit
  Initially 0
  When page is referenced, set to 1 by HW
To replace a page
  The first frame encountered with use bit 0 is replaced
  During the search for replacement, each use bit set to 1 is changed to 0 by OS
Note: if all bits set  FIFO

## Slide 56: Example Clock Policy

## Slide 57: Example Clock Policy

## Slide 58: Comparison of Basic Replacement Algorithms

## Slide 59: Comparison of Basic Replacement Algorithms

## Slide 60: Enhancement of Clock/Second Chance
Clock algorithm can be made more powerful by using more bits
  Use reference bit (R) and modify bit (M) as an ordered pair
With R and M bits, the following four classes are possible
  Class 0: Neither recently used nor modified (R=0, M=0)
    Best page to replace
  Class 1: Not recently used but modified (R=0, M=1)
    The page will need to be written out before replacement
  Class 2: Recently used but clean (R=1, M=0)
    Probably page will be used again soon
  Class 3: Recently used and modified (R=1, M=1)
    Probably page will be need soon and disk I/O is required to write page
Replacement strategy
  Replace the first page encountered in the lowest non empty class

## Slide 61: Enhancement of Clock/Second Chance
When a process starts
  All its page entries are marked as not referenced and not modified
When a page is referenced
  The R (reference) bit is set
When the page is later written to
  The M (modified) bit is set
Difference to clock algorithm
  Preference are given to pages that have been modified to reduce I/O

## Slide 62: Any Question So Far?