## Slide 1: Computer Networks
Week11_Lecture1 (Chapter3)
Transport Layer
Subhan Ullah, PhD
subhan.ullah@nu.edu.pk
BS(Computer Science) Spring-2024

## Slide 2: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
Principles of congestion control
TCP congestion control

## Slide 3: TCP: overview RFCs: 793,1122, 2018, 5681, 7323
cumulative ACKs
pipelining:
    TCP congestion and flow control set window size
connection-oriented:
  handshaking (exchange of control messages) initializes sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
    one sender, one receiver
reliable, in-order byte stream:
    no “message boundaries"
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
Notes: Typical MSS is 1460 bytes

## Slide 4: TCP segment structure
source port #
dest port #
32 bits
not
used
receive window
flow control: # bytes receiver willing to accept
sequence number
segment seq #: counting bytes of data into bytestream (not segments!)
application
data
(variable length)
data sent by application into TCP socket
A
acknowledgement number
ACK: seq # of next expected byte; A bit: this is an ACK
options (variable length)
TCP options
head
len
length (of TCP header)
checksum
Internet checksum
RST, SYN, FIN: connection management
F
S
R
Urg data pointer
P
U
C
E
C, E: congestion notification

## Slide 5: TCP sequence numbers, ACKs
Sequence numbers:
  byte stream “number” of first byte in segment’s data
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from receiver
A
sent
ACKed
sent, not-yet ACKed
(“in-flight”)
usable
but not
yet sent
not
usable
window size
N
  sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from sender
Acknowledgements:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say, - up to implementor

## Slide 6: MSS and MTU
The maximum amount of data in a segment is limited by the maximum segment size (MSS)
The MSS is typically set by first determining (the so-called maximum transmission unit, MTU)
  MSS+ TCP/IP header when encapsulated in an IP datagram) will fit into a single link-layer frame
Notes: the length of the largest link-layer frame that can be sent by the local sending host
FCS: Frame check sequence
ETH: Ethernet

## Slide 7: MSS and MTU
The MSS limits the maximum size of a segment’s data field
It is more or less a physical limit
It is specified for each link separately
MTU reduction can occur elsewhere in the communication path
Notes: Fiber Distributed Data Interface (FDDI)
Fiber Distributed Data Interface is a standard for data transmission in a local area network. It uses optical fiber as its standard underlying physical medium, although it was also later specified to use copper cable, in which case it may be called CDDI, standardized as TP-PMD, also referred to as TP-DDI.
MAC Service Data Unit (MSDU)
X.25 is an ITU-T standard protocol suite for packet-switched data communication in wide area networks. It was originally defined by the International Telegraph and Telephone Consultative Committee in a series of drafts and finalized in a publication known as The Orange Book in 1976.

## Slide 8: TCP Send/Receive buffers
The client process passes a stream of data through the socket
Once the data passes through the Socket, the data is in the hands of TCP running in the client
TCP directs this data to the connection’s send buffer, which is one of the buffers that is set aside during the initial three-way handshake
From time to time, TCP will grab chunks of data from the send buffer and pass the data to the network layer

## Slide 9: TCP connection
TCP connection consists of
  Buffers and variables
  a socket connection to a process in one host, and another set of buffers, variables, and a socket connection to a process in another host
Nothing is stored in the network elements (routers, switches, and repeaters) between the hosts

## Slide 10: TCP segment structure (Flags)
PUSH Flag
  The sending application informs TCP that data should be sent immediately
  The PSH flag in the TCP header informs the receiving host that the data should be pushed up to the receiving application immediately
Urgent Data
  DEL or CTRL-C to break off a remote computation
  Use URGENT flag – Transmit everything right now
  Receiving application is interrupted
Notes: PSH and the PUSH function
When you send data, your TCP buffers it. So if you send a character it won't send it immediately but wait to see if you've got more. But maybe you want it to go straight on the wire: this is where the PUSH function comes in. If you PUSH data your TCP will immediately create a segment (or a few segments) and push them.
But the story doesn't stop here. When the peer TCP receives the data, it will naturally buffer them it won't disturb the application for each and every byte. Here's where the PSH flag kicks in. If a receiving TCP sees the PSH flag it will immediately push the data to the application.

## Slide 11: Sequence Numbers
TCP views data as an unstructured, but ordered, stream of bytes
Sequence numbers are over the stream of transmitted bytes and not over the series of transmitted segments
The sequence number for a segment is therefore the byte-stream number of the first byte in the segment
A process in Host A wants to send a stream of data to a process in Host B
Example: The TCP in Host A will implicitly number each byte in the data stream
  For a file consisting of 500,000 bytes,
  MSS being 1,000 bytes, and that the first byte of the data stream is numbered 0
  TCP constructs 500 segments out of the data stream

## Slide 12: TCP Sequence Numbers
The first segment gets assigned sequence number 0, the second segment gets assigned sequence number 1,000, the third segment gets assigned sequence number 2,000, and so on

## Slide 13: Full duplex
TCP is full-duplex, so that Host A may be receiving data from Host B while it sends data to Host B (as part of the same TCP connection).
Data for B
A
B
Data for A
ACK
ACK
Notes: Simplex, half duplex and full duplex

## Slide 14: Acknowledgment numbers (Example)
Host A has received all bytes numbered 0 through 535 from B
Host A has also received another segment containing bytes 900 through 1,000
  For some reason Host A has not yet received bytes 536 through 899
  What does Host A put in the acknowledgment number field of the next segment it sends to B?
A’s next segment to B will contain 536 in the acknowledgment
number field

## Slide 15: Another example
A sends a segment to B, what would B put in the Ack sequence number in the next segment it sends to A?
  next byte Host B is expecting from Host A
A sends a segment to B, what would A put in the Ack sequence number in the next segment it sends to B?
  next byte Host A is expecting from Host B
  Host A has received all bytes numbered 0 through 535 from B
  Host A is waiting for byte 536 and all the subsequent bytes in Host B’s data stream
What does Host A put in the acknowledgment number field of the next segment it sends to B?
  Host A puts 536 in the acknowledgment number field of the segment it sends to B

## Slide 16: Out of order segments
TCP only acknowledges bytes up to the first missing byte in the stream, TCP is said to provide cumulative acknowledgments
For out of order segments it can either discard them or buffer them (the approach actually taken in practice)

## Slide 17: The seg/ack numbers base
we assumed that the initial sequence number was zero
In truth, both sides of a TCP connection randomly choose an initial sequence number
Why?
  This is done to minimize the possibility of a segment that is still present in the network from an earlier, already-terminated connection between two hosts is mistaken for a valid segment in a later connection between these same two hosts (which also happen to be using the same port numbers as the old connection)
Notes: This is done to minimize the possibility that a segment that is still present in the network from an earlier, already-terminated connection between two hosts is mistaken for a valid segment in a later connection between these same two hosts (which also happen to be using the same port numbers as the old connection)

## Slide 18: TCP sequence numbers, ACKs
host ACKs receipt of echoed ‘C’
host ACKs receipt of‘C’, echoes back ‘C’
simple telnet scenario
Host B
Host A
User types‘C’
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
Notes: Section E and F covered
Section D covered: 11-18-2021
The key thing to note here is that the ACK number (43) on the B-to-A segment is one more than the sequence number (42) on the A-to-B segment that triggered that ACK…
Similarly, the ACK number (80) on the last A-to-B segment is one more than the sequence number (79) on the B-to-A segment that triggered that ACK
Telnet IP address
Bidirectional and using port number 23.
To check the port on a remote system: telnet IP-address port# i.e., telnet 192.168.10.10 443

## Slide 19: TCP round trip time, timeout
Q: how to set TCP timeout value?
longer than RTT, but RTT varies!
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT:measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  average several recent measurements, not just current SampleRTT

## Slide 20: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
exponential weighted moving average (EWMA)
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)
Notes: This is how TCP re-computes the estimated RTT each time a new SampleRTT is taken.
The process is knows as an exponeitally weighted moving average, shown by the equation here.
<say it>
Where alpha reflects the influence of the most recent measurements on the estimated RTT; a typical value of alpha used in implementaitons is .125
The graph at the bottom show measured RTTs beween a host in the Massachusetts and a host in France, as well as the estimated, “smoothed” RTT

## Slide 21: TCP round trip time, timeout
timeout interval: EstimatedRTT plus “safety margin”
  large variation in EstimatedRTT: want a larger safety margin
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”
DevRTT = (1-)*DevRTT + *|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
DevRTT: EWMA of SampleRTT deviation from EstimatedRTT:
For Numerical examples the sequence of steps to follow are.
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
DevRTT = (1-)*DevRTT + *|SampleRTT-EstimatedRTT|
TimeoutInterval = EstimatedRTT + 4*DevRTT
Notes: Given this value of the estimated RTT, TCP computes the timeout interval to be the estimated RTT plus a “safety margin”
And the intuition is that if we are seeing a large variation in SAMPLERTT – the RTT estimates are fluctuating a lot - then we’ll want a larger savety margin
So TCP computes the Timeout interval to be the Estimated RTT plus 4 times a measure of deviation in the RTT.
The deviation in the RTT is computed as the eWMA of the difference between the most recently measured SampleRTT from the Estimated RTT

## Slide 22: TCP Sender (simplified)
event: data received from application
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unACKed segment
  expiration interval: TimeOutInterval
event: timeout
retransmit segment that caused timeout
restart timer
event: ACK received
if ACK acknowledges previously unACKed segments
  update what is known to be ACKed
  start timer if there are still unACKed segments
Notes: Given these details of TCP sequence numbers, acks, and timers, we can now describe the big picture view of how the TCP sender and receiver operate
You can check out FSMs in book; let’s just give an English text description here and let’s start with the sender.

## Slide 23: TCP Receiver: ACK generation [RFC 5681]
Event at receiver
arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
arrival of in-order segment with
expected seq #. One other
segment has ACK pending
arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
arrival of segment that
partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single cumulative
ACK, ACKing both in-order segments
immediately send duplicate ACK,
indicating seq. # of next expected byte
immediate send ACK, provided that
segment starts at lower end of gap
Notes: Rather than immediately ACKnowledge this segment, many TCP implementations will wait for half a second for another in-order segment to arrive, and then generate a single cumulative ACK for both segments – thus decreasing the amount of ACK traffic. The arrival of this second in-order segment and the cumulative ACK generation that covers both segments is the second row in this table.

## Slide 24: TCP: retransmission scenarios
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
Seq=92, 8 bytes of data
ACK=100
X
ACK=100
timeout
premature timeout
Host B
Host A
Seq=92, 8
bytes of data
ACK=120
timeout
ACK=100
ACK=120
SendBase=100
SendBase=120
SendBase=120
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
SendBase=92
send cumulative
ACK for 120
Notes: To cement our understanding of TCP reliability, let’s look a a few retransmission scenarios
In the first case a TCP segments is transmited and the ACK is lost, and the TCP timeout mechanism results in another copy of being transmitted and then re-ACKed a the sender
In the second example two segments are sent and acknowledged, but there is a premature timeout e for the first segment, which is retransmitted. Notet that when this retransmitted segment is received, the receiver has already received the first two segments, and so resends a cumulative ACK for both segments received so far, rather than an ACK for just this fist segment.

## Slide 25: TCP: retransmission scenarios
cumulative ACK covers for earlier lost ACK
Host B
Host A
Seq=92, 8 bytes of data
Seq=120, 15 bytes of data
Seq=100, 20 bytes of data
X
ACK=100
ACK=120
Notes: Section F covered: 19-11-2021
And in this last example, two segments are again transmitted, the first ACK is lost but the second ACK, a cumulative ACK arrives at the sender, which then can transmit a third segment, knowing that the first two have arrived, even though the ACK for the first segment was lost

## Slide 26
Thank You All

?
A note on the origin of these ppt slides:
All material copyright 1996-2020 J.F Kurose and K.W. Ross, All Rights Reserved
These slides are freely provided by the book authors and it represents a lot of work on their part. We would like to thank J.F Kurose and K.W. Ross.
Transport Layer: 3-150
Notes: Section F and G ended